## Slide 1
VELMOD-4b
A new regional velocity model for the Netherlands
March 2019
contact-norway@estimages.com Tel: + 47 22 60 02 85
Prediction improvement: up to 30%

## Slide 2
Timeline
February 2017
Agreement between Estimages and TNO
March 2017
End of data integration in the project
October 2017
May 2018
November 2018
Completion of VELMOD-4b
Pilot Project
Completion of VELMOD-4a
February 2019
Evaluation by TNO (blind wells)

## Slide 3
Key features
PREDICTION IMPROVEMENT
+5% to +30% in the intervals (blind wells estimation)
100 000 km²
179
136
1642
9
Area
3D seismic velocity data sets
2D seismic velocity data sets
Wells
Regional horizons
Integration of seismic velocities
VELMOD-4b is the first VELMOD integrating seismic velocities. The use of seismic velocities reduces prediction errors in areas with no wells.
New data
VELMOD-4b integrates the latest seismic and well data available over the Netherlands (onshore and offshore).
Optimized multi-variate model (M-GS® technology)
VELMOD-4b is the first VELMOD to propose a VINT model reconciling well time-depth functions, well tops and horizons. Geostatistical parameters are determined layer by layer through a prediction errors minimization process.

## Slide 4
Flowchart
RAW SEISMIC VELOCITIES
2D & 3D
WELL TIME DEPTH FUNCTIONS
(checkshots, sonics...)
HORIZONS (TWT)
WELL TOPS
MERGE SEISMIC VELOCITY VOLUME
3D M-GS® GRIDDING
(NON STATIONARY KRIGING)
2
QC, CONDITIONING,
GEOSTATISTICAL FILTERING
QUALIFIED SEISMIC VELOCITIES
2D & 3D
1
CALIBRATED SEISMIC VELOCITY VOLUME
3D M-GS® CALIBRATION
STRATIGRAPHIC GRID
3
VELMOD-4a
AUXILIARY VARIABLE
LAYER CAKE, V0-k PARAMETERIZATION
Independant TNO process
V0, k & VINT AT WELL LOCATIONS
V0 & VINT SPATIALIZATION
M-GS® CO-KRIGING
4
V0, VINT FOR EACH FORMATION
VELMOD-4b
VINT RESIDUAL CALIBRATION
FKED
5
V0, VINT FOR EACH FORMATION
VELMOD-4b
FINAL
AUXILIARY VARIABLE
VINT AT WELL LOCATIONS

## Slide 5
Formations
NU
Upper North Sea Group
NLM
Middle and Lower North Sea Group
CK
Chalk Group
KN
Rijnland Group
RNB
Upper and Lower Germanic Trias Group
ZE
Zechstein
SAT
Schieland and Altena Group

## Slide 6
VELMOD-4 building

## Slide 7
Flowchart
RAW SEISMIC VELOCITIES
2D & 3D
WELL TIME DEPTH FUNCTIONS
(checkshots, sonics...)
HORIZONS (TWT)
WELL TOPS
MERGE SEISMIC VELOCITY VOLUME
3D M-GS® GRIDDING
(NON STATIONARY KRIGING)
2
QC, CONDITIONING,
GEOSTATISTICAL FILTERING
QUALIFIED SEISMIC VELOCITIES
2D & 3D
1
CALIBRATED SEISMIC VELOCITY VOLUME
3D M-GS® CALIBRATION
STRATIGRAPHIC GRID
3
VELMOD-4a
AUXILIARY VARIABLE
LAYER CAKE, V0-k PARAMETERIZATION
Independant TNO process
V0, k & VINT AT WELL LOCATIONS
V0 & VINT SPATIALIZATION
M-GS® CO-KRIGING
4
V0, VINT FOR EACH FORMATION
VELMOD-4b
VINT RESIDUAL CALIBRATION
FKED
5
V0, VINT FOR EACH FORMATION
VELMOD-4b
FINAL
AUXILIARY VARIABLE
VINT AT WELL LOCATIONS
RAW SEISMIC VELOCITIES
2D & 3D
QC, CONDITIONING,
GEOSTATISTICAL FILTERING
QUALIFIED SEISMIC VELOCITIES
2D & 3D
1

## Slide 8
QC & conditioning of the seismic velocities
Qualified data base
Standard geostatistical QC of the 2D and 3D seismic velocity data sets
(statistics, variographic analysis…)
Resolution preserved
3D geostatistical filtering
No smoothing operator such as gaussian or median filter
etc.

## Slide 9
QC & conditioning of the seismic velocities
RAW
FILTERED
3D geostatistical filtering

## Slide 10
Flowchart
RAW SEISMIC VELOCITIES
2D & 3D
WELL TIME DEPTH FUNCTIONS
(checkshots, sonics...)
HORIZONS (TWT)
WELL TOPS
MERGE SEISMIC VELOCITY VOLUME
3D M-GS® GRIDDING
(NON STATIONARY KRIGING)
2
QC, CONDITIONING,
GEOSTATISTICAL FILTERING
QUALIFIED SEISMIC VELOCITIES
2D & 3D
1
CALIBRATED SEISMIC VELOCITY VOLUME
3D M-GS® CALIBRATION
STRATIGRAPHIC GRID
3
VELMOD-4a
AUXILIARY VARIABLE
LAYER CAKE, V0-k PARAMETERIZATION
Independant TNO process
V0, k & VINT AT WELL LOCATIONS
V0 & VINT SPATIALIZATION
M-GS® CO-KRIGING
4
V0, VINT FOR EACH FORMATION
VELMOD-4b
VINT RESIDUAL CALIBRATION
FKED
5
V0, VINT FOR EACH FORMATION
VELMOD-4b
FINAL
AUXILIARY VARIABLE
VINT AT WELL LOCATIONS
MERGE SEISMIC VELOCITY VOLUME
3D M-GS® GRIDDING
(NON STATIONARY KRIGING)
2
QUALIFIED SEISMIC VELOCITIES
2D & 3D

## Slide 11
3D merge of the seismic velocities
Priority rules
Consistency analysis
between the qualified seismic velocity datasets
Merge
In overlap areas definition of priority rules such as 3D > 2D
Merge by 3D non-stationary factorial kriging driven by the regional structure (M-GS®)

## Slide 12
3D merge of the seismic velocities
m/s
Inst. Vel - Time-slice 2sTWT

## Slide 13
Flowchart
RAW SEISMIC VELOCITIES
2D & 3D
HORIZONS (TWT)
WELL TOPS
MERGE SEISMIC VELOCITY VOLUME
3D M-GS® GRIDDING
(NON STATIONARY KRIGING)
2
QC, CONDITIONING,
GEOSTATISTICAL FILTERING
QUALIFIED SEISMIC VELOCITIES
2D & 3D
1
CALIBRATED SEISMIC VELOCITY VOLUME
3D M-GS® CALIBRATION
STRATIGRAPHIC GRID
3
VELMOD-4a
AUXILIARY VARIABLE
LAYER CAKE, V0-k PARAMETERIZATION
Independant TNO process
V0, k & VINT AT WELL LOCATIONS
V0 & VINT SPATIALIZATION
M-GS® CO-KRIGING
4
V0, VINT FOR EACH FORMATION
VELMOD-4b
VINT RESIDUAL CALIBRATION
FKED
5
V0, VINT FOR EACH FORMATION
VELMOD-4b
FINAL
AUXILIARY VARIABLE
VINT AT WELL LOCATIONS
CALIBRATED SEISMIC VELOCITY VOLUME
3D M-GS® CALIBRATION
STRATIGRAPHIC GRID
3
VELMOD-4a
WELL TIME DEPTH FUNCTIONS
(checkshots, sonics...)
MERGE SEISMIC VELOCITY VOLUME

## Slide 14
3D calibration of the seismic velocities
Computation of the depth residuals
At wells, depth residuals = seismic depth minus TVD
Structural analysis
3D variographic analysis of the depth residuals
2 structures: short scale (difference of resolution between well and seismic information), mid/long scale (mainly due to regional vertical anisotropy)
Calibration
Seismic velocity volume calibrated to the wells by 3D FKED
(Factorial Kriging with External Drift)
Driven by the horizons

## Slide 15
3D calibration of the seismic velocities
m/s
Inst. Vel - Time-slice 2sTWT
Inst. Vel - Time-slice 2sTWT
m/s

## Slide 16
3D calibration of the seismic velocities
Vint (m/s)
TWT (ms)
P01-04
Basemap
Vint (m/s)
TWT (ms)
OBD-01
Well velocity
Merge
Calibrated
Well velocity
Merge
Calibrated

## Slide 17
Flowchart
RAW SEISMIC VELOCITIES
2D & 3D
WELL TIME DEPTH FUNCTIONS
(checkshots, sonics...)
HORIZONS (TWT)
WELL TOPS
MERGE SEISMIC VELOCITY VOLUME
3D M-GS® GRIDDING
(NON STATIONARY KRIGING)
2
QC, CONDITIONING,
GEOSTATISTICAL FILTERING
QUALIFIED SEISMIC VELOCITIES
2D & 3D
1
CALIBRATED SEISMIC VELOCITY VOLUME
3D M-GS® CALIBRATION
STRATIGRAPHIC GRID
3
VELMOD-4a
AUXILIARY VARIABLE
LAYER CAKE, V0-k PARAMETERIZATION
Independant TNO process
V0, k & VINT AT WELL LOCATIONS
V0 & VINT SPATIALIZATION
M-GS® CO-KRIGING
4
V0, VINT FOR EACH FORMATION
VELMOD-4b
VINT RESIDUAL CALIBRATION
FKED
5
V0, VINT FOR EACH FORMATION
VELMOD-4b
FINAL
AUXILIARY VARIABLE
VINT AT WELL LOCATIONS
AUXILIARY VARIABLE
LAYER CAKE, V0-k PARAMETERIZATION
Independant TNO process
V0, k & VINT AT WELL LOCATIONS
V0 & VINT SPATIALIZATION
M-GS® CO-KRIGING
4
V0, VINT FOR EACH FORMATION
VELMOD-4b
WELL TIME DEPTH FUNCTIONS
(checkshots, sonics...)
CALIBRATED SEISMIC VELOCITY VOLUME
VELMOD-4a

## Slide 18
Vint gridding
ILLUSTRATION ON THE CHALK
Cross-variogram
Variogram
Variogram
lag (m)
lag (m)
lag (m)
variability (m²/s²)
variability (m²/s²)
variability (m²/s²)
Vint_VELMOD-4a
Vint_well
Vint_well vs Vint_VELMOD-4a
Correlation 70%
m/s
Chalk fm – Interval velocity
CO-KRIGING

## Slide 19
HORIZONS (TWT)
Flowchart
RAW SEISMIC VELOCITIES
2D & 3D
WELL TIME DEPTH FUNCTIONS
(checkshots, sonics...)
WELL TOPS
MERGE SEISMIC VELOCITY VOLUME
3D M-GS® GRIDDING
(NON STATIONARY KRIGING)
2
QC, CONDITIONING,
GEOSTATISTICAL FILTERING
QUALIFIED SEISMIC VELOCITIES
2D & 3D
1
CALIBRATED SEISMIC VELOCITY VOLUME
3D M-GS® CALIBRATION
STRATIGRAPHIC GRID
3
VELMOD-4a
AUXILIARY VARIABLE
LAYER CAKE, V0-k PARAMETERIZATION
Independant TNO process
V0, k & VINT AT WELL LOCATIONS
V0 & VINT SPATIALIZATION
M-GS® CO-KRIGING
4
V0, VINT FOR EACH FORMATION
VELMOD-4b
VINT RESIDUAL CALIBRATION
FKED
5
V0, VINT FOR EACH FORMATION
VELMOD-4b
FINAL
AUXILIARY VARIABLE
VINT AT WELL LOCATIONS
HORIZONS (TWT)
VINT RESIDUAL CALIBRATION
FKED
5
V0, VINT FOR EACH FORMATION
VELMOD-4b
FINAL
AUXILIARY VARIABLE
VINT AT WELL LOCATIONS
WELL TOPS
V0, VINT FOR EACH FORMATION
VELMOD-4b

## Slide 20
Vint rescaling
ILLUSTRATION ON THE CHALK
Cross-variogram
Variogram
Variogram
lag (m)
lag (m)
lag (m)
variability (m²/s²)
variability (m²/s²)
variability (m²/s²)
Vint_VELMOD-4b
Vint from well tops
Vint_well vs Vint_VELMOD-4b
m/s
Chalk fm – Interval velocity
FACTORIAL CO-KRIGING
of the large scale structure

## Slide 21
VELMOD-4 evaluation

## Slide 22
Blind wells testing
TNO has performed a comparison of the residual thickness errors with a dataset of 3 017 blind wells for both VELMOD-3 and VELMOD-4b.
Formation | VELMOD-3 | VELMOD-4b | Prediction improvement
NU | 27 | 25 | +7%
NLM | 36 | 25 | +30%
CK | 42 | 31 | +26%
KN | 32 | 27 | +16%
SAT | 28 | 23 | +18%
RNB | 38 | 36 | +5%
Comparison with VELMOD-3
Blind wells
Standard deviation of the depth error (m)

## Slide 23
Deliverables

## Slide 24
Deliverables
Seismic velocities
Regional velocity model
For each seismic velocity data set, 2D and 3D:
raw seismic velocity data file / standardized ASCII format
seismic velocity QC report
VELMOD-4a: 3D velocity model / 1km x 1km x 40ms
VELMOD-4b: V0, VINT for each geological layer (only VINT for the Zechstein fm) / 1km x 1km
depth converted surfaces / 250m x 250m
A specific grid mesh can be suggested
Report
VELMOD-4b full study report: description of data, models and parameters used for building the regional velocity model covering onshore and offshore Netherlands.

## Slide 25
Appendix
VELMOD-4 formations

## Slide 26
Upper North Sea Group
VINT ESTIMATION
VELMOD-3
VELMOD-4a
VELMOD-4b

## Slide 27
Comparison with VELMOD-3
NU (Upper North Sea Group)

## Slide 28
Middle & Lower North Sea Group
VINT ESTIMATION
VELMOD-3
VELMOD-4a
VELMOD-4b

## Slide 29
Comparison with VELMOD-3
NLM (Middle and Lower North Sea Group)

## Slide 30
Chalk Group
VINT ESTIMATION
VELMOD-3
VELMOD-4a
VELMOD-4b

## Slide 31
Comparison with VELMOD-3
CK (Chalk Group)

## Slide 32
Rijnland Group
VINT ESTIMATION
VELMOD-3
VELMOD-4a
VELMOD-4b

## Slide 33
Comparison with VELMOD-3
KN (Rijnland Group)

## Slide 34
Schieland & Altena Group
VINT ESTIMATION
VELMOD-3
VELMOD-4a
VELMOD-4b
No map available

## Slide 35
Comparison with VELMOD-3
S+AT (Schieland and Altena Group)

## Slide 36
Trias Group
VINT ESTIMATION
VELMOD-3
VELMOD-4a
VELMOD-4b

## Slide 37
Comparison with VELMOD-3
RB+RN (Lower and Upper Germanic Trias Group)

## Slide 38
Zechstein Group
VINT ESTIMATION
VELMOD-3
VELMOD-4a
VELMOD-4b