## Slide 1: Model approach to future offshore exploration Peter Rosenkranz Utrecht 15 January 2009

## Slide 2
We need to know the oil price

## Slide 3
We need to know the rig rate (development cost)

## Slide 4
We need to know the prospects

## Slide 5
We need to know the activity level
“Predicting is very difficult, especially if it is about the future” (Niels Bohr)

## Slide 6: ProSim: Monte Carlo simulation Model
The model generates a field development plan for every prospect taking into account:
- Reserves
- Distance to infrastructure
- Productivity
- Abandonment data and Opex of host platform
In case of ‘success’ the model generates new infrastructure that can be used by the remaining prospects
The decision to drill is based on a full economic evaluation and EMV or RVIR screening criterion.

## Slide 7: Opex host platform and Abandonment deferment
Production profile is added to existing profile of host platform.
New abandonment date is when sum of profiles becomes lower than minimum production
Fixed Opex platform is shared on basis of throughput

## Slide 8: Model Input
Prospect database (TNO) (POS, LSV,MSV,HSV, productivity, xy-coordinates)
Platform database (abandonment date, Opex, xy coordinates)
Exploration & development cost parameters
Economic analyses (Capex, Opex, production profile, EMV, RVIR)
Screening Ranking Criterion (per operator)
Activity level (per operator)
Oil (gas) price

## Slide 9: ProSim Work flow
Year= n
Calculate EMV / RVIR for all prospects
  Select prospect for drilling
  In case of Succes
    Draw a reserve from volume distribution
    Recalculate economics
    Adjust abandonment date host platform
    Adjust infrastructure database in case of
    platform development
Go to next well
Go to next Year
If there are no prospects / platforms left then stop

## Slide 10: ProSim Output
Future reserves + production profile
Cashflows for State and Licensee
ProSim may give answers on strategic issues such as:
    Is the level of exploration drilling sufficient to ensure that all economic prospects are drilled in time?
What is the effect of (fiscal) stimulation measures?

## Slide 11: Results
With 5 wells/year there will be some 70 wells in total
being drilled in 14 years.

## Slide 12: Results

## Slide 13: Results

## Slide 14: Results

## Slide 15: Conclusions offshore exploration
Optimal number of exploration wells : > 10 / year
End of exploration for 100 $/bbl
  5 wells / year : 2041 (2048)
  10 wells / year : 2028 (2032)
End of exploration for 50 $/bbl
  5 wells / year : 2019 (2023 with proposed measures)
  10 wells / year : 2015 (2018)

## Slide 16: Conclusions offshore exploration
Remarks:
The conclusions may be too optimistic because:
  No back-out in the calculations
  No limitation in access, processing and transport
The conclusions may be too conservative because:
  The infrastructure will be longer available then we think now
  New prospects will be generated